Gis data structure in
the Inno Project

Version	Data	Author
1	30/06/15	Roberto Demontis

# Introduction
Scalability and flexibility of web applications, data accessibility and security are open issues tightly bound to technological development. Such needs have been addressed by the INNO project by developing a suite of tools and in house solutions to exploit large geo-data sets, made available through a Storage Data Infrastructure (SDI). Such tools are loosely coupled components that aim at addressing specific needs such as data management and accessibility. A service oriented architecture has been optimised for querying GIS based data with a NoSQL approach. The solution we propose was developed and positively tested for the management of large geo-data.
The solution is built on the use of vector tiles with different degree of resolution at different zoom levels. It increases the volume of the data to be managed but allows more speed loading tiles, flessibility in mobile devices data management and maintains the fine-grained information level of a WFS ( OGC Web Feature Server[1]). In this context the No-SQL choice ensures scalability and data replication depending on available resources.
[1] https://en.wikipedia.org/wiki/Web_Feature_Service
The No-SQL environment used for the SDI is Couchbase Server[2] Community Edition. The Gis data is loaded in a unique database, or bucket, named “Inno”. Each tile is very light and is stored within the NoSQL db as a JSON document using the pagination of the data for each tile. For that the features are ordered by a drawing priority based on its geometrical property (e.g. the area value for polygon). The vectorial tiles are accessed directly using the key value mechanism
[2] http://docs.couchbase.com/couchbase-manual-2.2/
The non-geometrical properties of the features is stored separately and indexed using a spatial index, a R-Tree, based on the bounding box of the features and accessed without a reduce() method.
The import of the data into the SDI can be performed using a tool named “innoImportShapefile” that can be found in the “Inno Web App” distribution. This tool is a set of shell scripts and ETL(Extract, Transform and Load) functions wrote in the pgsql language for the PostgreSQL environment. The functions perform the tiling of the Gis Data stored in a compressed Esri shapefile. The choice of Postgresql is due to the stability of the system in the elaboration of large set of data. Obviously the same result can be obtained and implemented using other language and environment.

# Gis data structure in the NoSQL database
All the data is stored in a unique database but, to determinate the gis layer of the data stored in a document is sufficent to read the key of it. In fact all the key of json documents of a specific gis layer start with the name of the layer with the convention:

Inno Type Name	Infos
Document Key	<name>':'<id_feature>
Example	“landuse:0001”
Description	document with non-geometrical properties of a feature
Inno Type Name	Layer
Document Key	<name>
Example	“landuse”
Description	Document with layer metadata
Inno Type Name	Tile
Document Key	<name>':'<x>('+'<dx>)':'<y>('+'<dy>)':'<zoom>':'<page>
Examples	“landuse:71181:50425:17” o “landuse:71012+0:50225+3:17”
Description	Document with geometrical properties of a feature
Inno Type Name	Views
Document Key	<name>views
Example	landuseviews
Description	Design document with definition of indices

        Table 1: document keys used in the NoSql database
Where:
- x,y and zoom are the tile coordinates using Slippy Map TileNames[3]
  [3] http://wiki.openstreetmap.org/wiki/Slippy_map_tilenames
- dx and dy are extensions in tiles of x and y respectively that define a macrotile. A macro tile si a set of adiacent tiles.
- name is the name of the layer
- page (optional) is an integer (>1) indicating the page of the data of the tile (each page has dimension <= 25Kb)

### Structure of the document “Layer”
Name	Type	Description
_innoname_	Testo	Unique identifier of the layer (the key)
_bbox_	GeoJSon	Wgs84 bounding Box of the layer
description	Testo	Decription of the layer
vertices	Intero	Number of vertices
count	Intero	Number of features
type	Testo	A geometry type. It can be one of the following types: / “MULTIPOINT”, “POINT”, “MULTILINESTRING”, “LINESTRING”, “MULTIPOLYGON”, “POLYGON”
levels	Array<Level>	Property of zooms' level available
attributes	Array<Attribute>	Property of the non geometrical attribute of the layer

     Table 2: field of “Layer” document

Name	Type	Description
name	Testo	Name of the attribute
type	Testo	Type of the attribute

     Table 3: fields of the “Attribute” object in the “Layer” document

Name	Type	Description
zoom	Integer	level of zoom
tiles	Array<Integer>	Bbox in Slippy Map Tilenames coordinate: [xmin.ymin,xmax,ymax]

     Table 4: fields of the “Level“ object in the “Layer” document

### Structure of the document “Tile”
Name	Type	Description
Id	Testo	Unique identifier of the tile (the key)
_{layername}macrobbox{zoom}_	GeoJSON	The bbox in WGS84 of the tile (for macro-tile)
_bbox_	GeoJSON	The bbox in WGS84 of the tile (for simple tile)
page	integer	Page number in the data impagination for this tile
pages	integer	Number of pages of data for the tile
objs	Array[Element]	data element

###### Table 5: fields of the document “Tile”
Name	Type	Description
id	Testo	Unique identifier of the feature in the layer private of the layer name (the feature key)
g	Testo	Vectorial representation of geometry coordinates (see table 7)

     Table 6: fields of the “Level“ object in the“Tile” document

### Coding the coordinates of a geometry in a document “Tile”
The representation of a geometry è quite similar to the WKT[4]. It starts with the type code and put the coordinates round brackets:
[4] http://en.wikipedia.org/wiki/Well-known_text
Type Name	Type code	Structure
POINT	1	1(####)
LINEA	2	2(####...####)
POLIGONI	3	3((####..####),(####...####))

     Tabella 7: tipi di geometrie e loro rappresentazione
the coordinates are expressed with exadecimal values relative to the origin of the tile. So, because the tile is a 255x255 pixel in size, each vertex take 4 byte (if the document is not comprerssed)
Each coordinate can be transformed in a easy way in WGS84 latitude and longitude or in simple Mercator x and y using the coordinates of the origin of the tile and the Slippy Map Tilenames rules.

### Documenti “Infos”
Name	Type	Description
_{layername}bbox_	GeoJSON	The bbox in WGS84 of the feature
{lattribute name}	attribute type	A Field with name and value of an attribute
.....	....	....
{lattribute name}	attribute type	A Field with name and value of an attribute

###### Tabella 7: campi json nel documento “Infos”
### Documenti “Views”
A document of type “Views” is a particular json document, called in couchbase “Design Document” that defines the spatial indices that manage the access to “Infos” and “Layer” documents.

# Data Access
The Inno Web App expose the RestFul interface below

Inno Request Name	List
http://your_server/inno/json/list(/<page>)
It returns a json document with an array of layer's metadata ( documents of the type 'Layer'
Inno Request Name	GetLayer
http://your_server/inno/json/layer/<name>
It returns a json document of the type 'Layer'
Inno Request Name	GetTile
http://your_server/inno/json/tile/<name>/<x>/<y>/<zoom>(/<page>)
It returns the json document of the vectorial tile (a document of the type “Tile”)
Inno Request Name	GetInfos
http://your_server/inno/json/infos/<name>/<x>/<y>/<zoom>(/<page>)
It returns a json document with an array of documents of the type 'Info' of the features present in a tile
Inno Request Name	GetValue
http://your_server/inno/json/value/<name>/<attribute>/<x>/<y>/<zoom>(/<page>)
It returns a json document with an array of values of the specified attribute of the features present in a tile

# Il Tool InnoImportShape
InnoImportShapeFile is a simple set of script for the Linux environmet (Ubuntu Server 14.04) that permits to load a gis layer stored in a Esri shape file format into couchbase.
The tool depends on: postgresql (v:9.3), postgis, gzip, tar, zip, unzip, bash, couchbase (only for the tool cbdocloader).
To configure the tool first write the correct parameters in the file:
/path_to/innotool/inno_set_global.sh
The next step is to create a local postgresql database with postgis functionalities and then add to it the etl_functions with the comand:
psql -f /path_to/innotool/etl_functions.sql -d your_database
Finally to perform the import execute the command
      /path_to/innotool/inno_import.sh new_layer_name path_to_compressed_shapefile
 where
 - new_layer_name : The name of the new layer
- path_to_compressed_shapefile : The compressed shapefile
The Shapefile should have the following properties:

- The shape layer must be compressed with zip must contain at least three files with the extension .shp, .shx and .dbf with the same name.
- geometries should be of the same type, one of: point, line, polygon, multipoint, multiline, multipolygon
geometries must follow the OGC guidelines that can be found at the following link http://www.opengeospatial.org/standards/sfa
polygonal geometries must not have intersections
attribute names can not start with '_'
attribute names can not contain ':'
attribute name can not be 'gid'
Note1: A couchbase node should be visible from the server
Note2: The tiling of large layer ( over 1 GB of size ) can take many hours
Appendici
## Examples of response to a request
List Request
{"layers":[{"_innoname_":"comuni","_bbox_":{"type":"Polygon","coordinates":[[[8.130769799999999,38.859124],[8.130769799999999,41.3132405],[9.8270429,41.3132405],[9.8270429,38.859124],[8.130769799999999,38.859124]]]},"vertices":314610,"count":377,"type":"MULTIPOLYGON","attributes":[{"name":"gid","type":"integer"},{"name":"istat","type":"double precision"},{"name":"nome","type":"character varying"},{"name":"regione","type":"character varying"},{"name":"subregione","type":"character varying"}],"levels":[{"zoom":10,"tiles":[535,382,539,391]},{"zoom":11,"tiles":[1070,765,1079,783]},{"zoom":12,"tiles":[2140,1530,2159,1567]},{"zoom":13,"tiles":[4281,3061,4319,3134]},{"zoom":14,"tiles":[8562,6123,8639,6269]},{"zoom":15,"tiles":[17124,12247,17278,12539]},{"zoom":16,"tiles":[34248,24495,34556,25079]},{"zoom":17,"tiles":[68496,48990,69113,50158]}]}]}

### GetTile Request
{"_bbox_":{"type":"Polygon","coordinates":[[[8.08594,38.82259],[8.08594,39.09596],[8.4375,39.09596],[8.4375,38.82259],[8.08594,38.82259]]]}, "objs": [{"id":"085","g":"3((ff78ff79ff79ff79ff7aff7bff7cff7cfe7cfd7cfd7dfc7efb7efb7ffa7ffa7ef97ef97df87df87ef77ef67ef67ff57ff47ff47ef37ef37df37ef27ef17ef17ff07ff17ff07ff080f180f080f081f082f083ef83ee83ee82ee83ee82ed82ec82ec81eb81ea81ea80ea7fe97fe97ee87ee87de77de77ce77be77ae779e679e779e778e777e778e877e777e776e876e875e775e774e874e773e772e872e772e771e772e671e570e470e471e470e370e36fe26fe26ee26de26ce16be16ae169e069e169e069e068e067e066e166e066e166e066e166e065e165e065e064e164e064e063e163e063e062df62de62de61de60dd60dd61dc61dc60dc5fdc5edc5ddc5edb5ddb5cdb5ddb5cdb5bda5bda5adb5bdb5ada5ad95ad959d958da58da57db56da56d957d956d957d956d856d956d955d855d854d954d953d853d854d853d753d853d953da53d953d952da52da51d951d851d751d651d650d750d74fd64fd74fd74ed64ed64fd54fd44fd44ed34ed44ed44dd34dd34cd34bd24bd24ad14ad149d148d048d047cf47d047d046d045d046d045d145d144d244d243d143d243d242d342d442d441d440d43fd33fd33ed43ed43dd53dd53cd63cd63bd73bd73ad739d738d638d637d636d736d834d833d933d932d931da2fdb2edc2cdd2cde29df28e027e026e125e124e123e222e31fe41de51ae617e616e615e811e90fe90ee90dea0aeb09ee09ee08ef06f004f101f100fc00fd00fe00ff00ff00ff78))"},{"id":"158", "g":"3((9a009a0099009a00))"},{"id":"158", "g":"3((9800980098019701960195009500940093009800))"}, {"id":"158", "g":"3((8d008d008c008c018b018b008a008a01890189008800890088008d00))"},{"id":"427", "g":"3((ecd9edd9eddaeedaeedbeedceddcecdcecddebddebdceadbebdbebdaebd9ecd9))"}], "id":"comuni:535:391:10", "page":1, "pages":1}

### GetValue Request
{"subregione":[{"id":"comuni:158","v":"Sulcis-Iglesiente"},{"id":"comuni:249","v":"Sulcis-Iglesiente"},{"id":"comuni:085","v":"Sulcis-Iglesiente"},{"id":"comuni:427","v":"Sulcis-Iglesiente"},{"id":"comuni:112","v":"Sulcis-Iglesiente"}], "id":"comuni:535:391:10"}

### GetInfos Request
{
  "_comunibbox_": {
    "type": "Polygon",
    "coordinates": [
      [[8.13077,40.65175],[8.13077,40.8693],[8.6436,40.8693],
      [8.6436,40.65175],[8.13077,40.65175]]]
  },
  "gid": 128,
  "istat": 90064,
  "nome": "Sassari",
  "regione": "Sardegna",
  "subregione": "Sassarese",
  "id": "001"
}